## Slide 1: Marginal approach Rob Bailis – SEI Adrian Ghilardi - UNAM
ETHOSCon Jan 24-25, 2025
Timothy Akolamazima: CC-BY-SA-4.0

## Slide 2: Overview
Uncertainties – Improving MoFuSS
Marginal fNRB – New methods
https://ctrees.org/products/tree-level

## Slide 3: Uncertainties
Being n, the number of Monte Carlo realizations

## Slide 4: Uncertainty in Tool30
To use Tool30, you need to know:
Areas of different types forest
  Ideally areas of “trees outside forests” too
Woody biomass growth rates in each forest type
  Suggest 3 possible sources as well as “National studies or government data or official statistics”
Woodfuel demand (not covering today)
Recommended sources of data for forest growth (using mean annual increment – MAI)
TOOL30 Version 04.0 Data / Parameter table 5 (from Sept, 2022)

## Slide 5: Uncertainty in Tool30
2. IPCC AGB growth rates
(re)growth rates are not constant
  Very variable
  Higher in young and recently disturbed stands
  Uncertainty is included, but Tool30 ignores it
From IPCC’s “2019 Refinement to the 2006 IPCC Guidelines for National Greenhouse Gas Inventories”

## Slide 6: Uncertainty in Tool30 – how large is it?
We built a simple excel model using data recommended by Tool30 to calculate the uncertainty in fNRB using Standard Deviations in MAI from the IPCC

## Slide 7: Marginal fNRB
https://thoughtf20.classes.ryansafner.com/slides/3.2-slides#26
What the heck are we talking about?
Common in Economics
  The effect of a unit change in one variable on another variable
  Utility, Cost/Revenue, Productivity
    Output is a non-linear function of inputs like capital and labor (top graph)
    An additional unit of input affects output differently depending on the quantity of inputs already being utilized (lower graph - blue line)

## Slide 8: Marginal fNRB
How does this apply to trees?
“Output” is woody biomass
MPi is Current Annual Increment (CAI)
  Inputs are sunlight, nutrients, and the trees …
“leaves are the forest’s photosynthetic factory”
But its not a direct analogy
  These plots show “time”, not inputs
  We’re not directly interested the growth curve
    We need to know how harvest leads to losses in stock
https://www.researchgate.net/publication/357163700_Growth_Equations_in_Forest_Research_Mathematical_Basis_and_Model_Similarities/figures?lo=1

## Slide 9: Marginal fNRB
Things get more complicated
Each country we assess has dozens of growth functions distributed across thousands to millions of pixels
  Harvest is very heterogenous
We’re using MoFuSS to “construct” a marginal fRNB function for each country:
Examples of growth functions used in different eco-regions

## Slide 10: Marginal fNRB
VERY preliminary results using Tanzania as a test case
  We ran 10 simulations changing demand uniformly by ± 5, ± 10, ± 15, ± 25, & ± 50%
Chart: 
| 279848812 | 414525150 | 466650762 | 492269056 | 517781855 | 542716642 | 566967238 | 590227464 | 612417174 | 656112561 | 745506924
 | 158813710 | 243145878 | 276858540 | 293668612 | 310671481 | 327417958 | 343852913 | 359674650 | 374710450 | 404340696 | 458697223
NRB as a function of wood harvest
fNRB and mfNRB as a function of wood harvest
Chart: fNRB and mfNRB (%)
| 414525150 | 466650762 | 492269056 | 517781855 | 542716642 | 566967238 | 590227464 | 612417174 | 656112561
mfNRB | 0.62618 | 0.64676 | 0.65617 | 0.66644 | 0.67161 | 0.67771 | 0.68021 | 0.6776 | 0.67811
fNRB | 0.58656 | 0.59329 | 0.59656 | 0.6 | 0.60329 | 0.60648 | 0.60938 | 0.61185 | 0.61627
mfNRB comes out 5-7% higher than fNRB

## Slide 11: Marginal fNRB – next steps
Repeat in additional countries using uniform changes in demand
  TZA is high fNRB, we’ll add a few others (e.g. MWI, SEN)
  Low fNRB countries
  Rapidly changing fuel mix (e.g. India, Kenya)
Examine the impact of non-uniform changes
  Only fuelwood (mainly subsistence)
  Only charcoal (fully commercial)
  Specific admin units

## Slide 12: Thank you!
Past and present funders
Team MoFuSS

## Slide 13: Uncertainty in Tool30
1. FAO’s 2000 Global Forest Resource Assessment
Why, in 2022, was the UNFCCC still recommending FAO data from 2000?
  More recent GFRA’s don’t include data in the same form
What’s the problem?
  Focused only on forest areas - not where most people harvest wood
An extreme example from Rwanda:
  GFRA only includes montane forest covering 12% of the country
  75% of Rwandans who collect fuelwood obtain it from private land and 88% travel less than 2km (MININFRA, 2020)

## Slide 14: Challenges using Tool30 – misleading or ambiguous data sources
Other sources have very limited coverage. E.g. FAO’s 2015 GFRA:
Only includes 11 countries in SSA
Has no breakdown by forest type
  Only conifer / broadleaf
  Inconsistent presentation of data
  No scientific sources cited
  No uncertainty provided
From FAO’s “2015 Global Forest Resource Assessment”
Take Kenya as an example:
1.3 m3/ha-yr for broadleaf forests
  < Mauritania ?!?!
0.9 dry-tons/ha-yr
lower than most IPCC data