## Slide 1: Generating Emission Reductions from Clean Cooking Interventions
Rob Bail is – SEI US
Adrian Ghilardi – UNAM
Stephen Pluymaekers – CCA
Dana Charon – Berkeley Air Monitoring Group
MoFuSS 2025 BeZero Workshop
Tuesday 05 November 2024

## Slide 2: What’s all the fuss about?
Chart: 
| 2020 | 2050
Asia | 1357.829 | 289.2232
Africa | 917.8162 | 1417.8721
Latin America | 70.7257 | 74.6594
Rest of world | 25.1028 | 36.3595
Today, about 2.3 billion people rely on woodfuels☨ for their energy needs (WHO)
  Top risk factor for illness and death
    2.6 million deaths in LMICs in 2021 (IHME) ✧
  1-2% of global climate-forcing ❊
  Large burden on household labor & budget
  Largest source demand for woody biomass
    50% of “roundwood” harvest burned as fuel (FAO)
    Potentially large driver of degradation (see appendix)
☨ From WHO’s Household Air Pollution database
Woodfuels as primary cooking fuel (2020 & 2050)
billions of people
The no. of woodfuel users in SSA is projected to grow by 450 million by 2050
* Woodfuels include unprocessed firewood, charcoal, and processed fuels like wood pellets
✧ More than Malaria, Tb, and HIV/AIDS combined
❊ Own calculations using methods described in Floess et al with updated inputs
Notes: What are NBS? (from Nature-based Solutions Initiative at Oxford)
Nature-based Solutions involve working with nature to address societal challenges, supporting human well-being and biodiversity locally. They include the protection, restoration or management of natural and semi-natural ecosystems; the sustainable management of aquatic systems and working lands; and integration of nature in and around our cities.
Malaria 0.75 M
Tb 1.2 M
HIV/AIDS 0.5 M
Total 2.5 M

## Slide 3: How much degradation?
From Pearson et al. (2017)
Woodfuels are the dominant driver of degradation in E Africa and S Asia
Bubble chart showing degradation emissions by region (the bubble size represents the relative magnitude of emissions)
Notes: This estimate is about 1.1% -- only considers LULUCF, not forcing from PICs

## Slide 4: MoFuSS: projecting changes in tree cover (2020-2030) *
*Modeling Fuelwood Savings Scenarios -- explore and download results at https://www.mofuss.unam.mx/mofuss-ds/
~ 390 ± 11 million tons of wood are lost annually
Resulting in net emissions of ~0.7 Gt CO2 / year

## Slide 5: Interventions attempt to reduce woodfuel demand by:
…introducing efficient wood and charcoal stoves
Engineered solid fuels
LPG
E-cooking
Ethanol
…promoting alternative fuels

## Slide 6: Carbon flows in the woodfuel life-cycle
Biomass growth
CO2
Harvesting
Adapted from Forrest Robinette - CCA
Notes: Here its worth stopping for a second for a brief tutorial on biomass and climate impacts. Start on the upper left…

## Slide 7: Carbon flows in the woodfuel life-cycle
Biomass growth
CO2
Harvesting
Physical labour, drudgery,
land cover change(?)
Livelihoods, Income
Adapted from Forrest Robinette - CCA
Notes: Here its worth stopping for a second for a brief tutorial on biomass and climate impacts. Start on the upper left…

## Slide 8: Carbon flows in the woodfuel life-cycle
Biomass growth
Biomass burning
(for charcoal there’s also pyrolisis and transport with additional emissions)
CO2
Harvesting
Adapted from Forrest Robinette - CCA
Physical labour, drudgery,
land cover change(?)
Livelihoods, Income
Notes: Here its worth stopping for a second for a brief tutorial on biomass and climate impacts. Start on the upper left…

## Slide 9: Carbon flows in the woodfuel life-cycle
Biomass growth
Biomass burning
(for charcoal there’s also pyrolisis and transport with additional emissions)
CO2
Harvesting
Adapted from Forrest Robinette - CCA
Energy services (cooked food, heat, etc)
Complete combustion
CO2
Climate impacts
Physical labour, drudgery,
land cover change(?)
Livelihoods, Income
Notes: Here its worth stopping for a second for a brief tutorial on biomass and climate impacts. Start on the upper left…

## Slide 10: Carbon flows in the woodfuel life-cycle
Biomass growth
Biomass burning
(for charcoal there’s also pyrolisis and transport with additional emissions)
CO2
Harvesting
Adapted from Forrest Robinette - CCA
Energy services (cooked food, heat, etc)
CH4, PM, BC & OC, CO, N2O, NOx NMHCs…
Incomplete combustion
Complete combustion
CO2
Health & more climate impacts
Climate impacts
Physical labour, drudgery,
land cover change(?)
Livelihoods, Income
Notes: Here its worth stopping for a second for a brief tutorial on biomass and climate impacts. Start on the upper left…

## Slide 11: Carbon flows in the woodfuel life-cycle
Biomass growth
Biomass burning
(for charcoal there’s also pyrolisis with additional emissions)
CO2
Harvesting
CO2
CO2 Seq
Net CO2
CH4, PM, BC & OC, CO, N2O, NOx NMHCs…
Some CO2 is stored by new plants and trees
Incomplete combustion
Some CO2 remains in the atmosphere
Complete combustion
Adapted from Forrest Robinette - CCA
Energy services (cooked food, heat, etc)
Health & climate impacts
Climate impacts
Physical labour, drudgery,
land cover change(?)
Livelihoods, Income
Two paths to climate impacts
Notes: Here its worth stopping for a second for a brief tutorial on biomass and climate impacts. Start on the upper left…

## Slide 12: Putting some numbers on the carbon flows
7%
1%
<<1%
Energy and carbon flows in an Indian mud chulha
From Smith et al. 2000
< 1%
~90%
9%
Notes: 1.4 kg CO2 (about 90% impact)
0.114 kg CO2e as methane (about 10% impact)

## Slide 13: Putting some numbers on the carbon flows (in CO2e)
Energy and carbon flows in an Indian mud chulha
From Smith et al. 2000
~ 90%
~ 10% wt’d by GWP
Proportions change if we account for regrowth
Notes: 1.4 kg CO2 (about 90% impact)
0.114 kg CO2e as methane (about 10% impact)

## Slide 14: One kilo of charcoal looks different…
6 kg wood
2.8 kg carbon
108 MJ
1 kg charcoal
800 g carbon
30MJ
NMHC
300 g carbon
Methane
60 g carbon
Carbon monoxide
250 g carbon
Particulates
70 g carbon
Carbon dioxide
900 g carbon
Brands & condensables
~400 g carbon
NMHC
5 g carbon
Methane
5 g carbon
Carbon monoxide
60 g carbon
Particulates
5 g carbon
Carbon dioxide
700 g carbon
Pyrolysis
Cooking
Using one kilo of charcoal emits 5.9 kg CO2 and 87 g of CH4 (2.3 kg CO2e)
  (also depends on tree regrowth)
Notes: 5.9 kg CO2 (about 70% impact)
0.87 g CO2e as methane (about 30% impact)
Nearly 70% is from pyrolysis

## Slide 15: An intervention in a Ugandan household (40%fNRB)
Urban charcoal users
750 kg charcoal / year (4.5 tons wood)
3.5 tons CO2e / yr
  Reduces 1.8t CO2e
  Adds 0.3 t CO2e from LPG
Net change is –1.5 t CO2e
Rural wood users
2.5 tons of wood / year
1.7 tons CO2e / yr
An LPG intervention reduces fuel consumption by 50%
  Reduces 0.9 t CO2e
  Adds 0.3 t CO2e from LPG
Net change is –0.6 t CO2e
Notes: Assumptions:
People use 500 kg wood or 150 kg charc per yr
HH uses 156 ÷ 2 kg of LPG/yr (1 ÷ 2 cylinder/month)

## Slide 16: Explanation of BURN fNRB method and differences with MoFuSS?

## Slide 17: Marginal fNRB
https://thoughtf20.classes.ryansafner.com/slides/3.2-slides#26
What the heck are we talking about?
Common in Economics
  The effect of a unit change in one variable on another variable
  Utility, Cost/Revenue, Productivity
    Output is a non-linear function of inputs like capital and labor (top graph)
    An additional unit of input affects output differently depending on the quantity of inputs already being utilized (lower graph - blue line)

## Slide 18: Marginal fNRB
How does this apply to trees?
“Output” is woody biomass
MPi is Current Annual Increment (CAI)
  Inputs are sunlight, nutrients, and the trees …
“leaves are the forest’s photosynthetic factory”
But its not a direct analogy
  These plots show “time”, not inputs
  We’re not directly interested the growth curve
    We need to know how harvest leads to losses in stock
https://www.researchgate.net/publication/357163700_Growth_Equations_in_Forest_Research_Mathematical_Basis_and_Model_Similarities/figures?lo=1

## Slide 19: Marginal fNRB
Things get more complicated
Each country we assess has dozens of growth functions distributed across thousands to millions of pixels
  Harvest is very heterogenous
We’re using MoFuSS to “construct” a marginal fRNB function for each country:
Examples of growth functions used in different eco-regions

## Slide 20: Marginal fNRB
VERY preliminary results using Tanzania as a test case
  We ran 10 simulations changing demand uniformly by ± 5, ± 10, ± 15, ± 25, & ± 50%
Chart: 
| 279848812 | 414525150 | 466650762 | 492269056 | 517781855 | 542716642 | 566967238 | 590227464 | 612417174 | 656112561 | 745506924
 | 158813710 | 243145878 | 276858540 | 293668612 | 310671481 | 327417958 | 343852913 | 359674650 | 374710450 | 404340696 | 458697223
NRB as a function of wood harvest
fNRB and mfNRB as a function of wood harvest
Chart: fNRB and mfNRB (%)
| 414525150 | 466650762 | 492269056 | 517781855 | 542716642 | 566967238 | 590227464 | 612417174 | 656112561
mfNRB | 0.62618 | 0.64676 | 0.65617 | 0.66644 | 0.67161 | 0.67771 | 0.68021 | 0.6776 | 0.67811
fNRB | 0.58656 | 0.59329 | 0.59656 | 0.6 | 0.60329 | 0.60648 | 0.60938 | 0.61185 | 0.61627
mfNRB comes out 5-7% higher than fNRB

## Slide 21: Marginal fNRB – next steps
Repeat in additional countries using uniform changes in demand
  TZA is high fNRB, we’ll add a few others (e.g. MWI, SEN)
  Low fNRB countries
  Rapidly changing fuel mix (e.g. India, Kenya)
Examine the impact of non-uniform changes
  Only fuelwood (mainly subsistence)
  Only charcoal (fully commercial)
  Specific admin units

## Slide 22: Extra slides

## Slide 23: Brief list of research on woodfuels and degradation
Ahrends et al (2010) “Predictable waves of sequential forest degradation and biodiversity loss spreading from an African city”
Hosonuma et al (2012) “An assessment of deforestation and forest degradation drivers in developing countries”
Ryan et al. (2014) “Quantifying the causes of deforestation and degradation…method and case study from central Mozambique”
McNicol et al (2018) “Carbon losses from deforestation and widespread degradation offset by extensive growth…”
Sedano et al (2016) “The impact of charcoal production on forest degradation: a case study in Tete, Mozambique”
Pearson et al. (2017) “Greenhouse gas emissions from tropical forest degradation: an underestimated source”

## Slide 24: Definitions
Deforestation
The conversion of forest to another land use or the long-term reduction of tree canopy cover below a minimum threshold.
Degradation
Changes that negatively affect the structure or function of forests, woodlands, or stands of trees, lowering their capacity to supply products and/or services.
(both adapted from FAO)
From Shapiro et al. (2020)
Notes: Deforestation:
Degradation:

## Slide 25: Example of charcoal-driven degradation…
Annual forest degradation from charcoal production (2008-2018)
NDVI images (top) and time series (bottom) in mopane woodlands comparing areas affected by charcoal production (blue squares) to unaffected areas over a 2-year period.
Notes: NDVI – (Normalized difference vegetation index) quantifies vegetation health using near-infrared (which is reflected by vegetation) and red light (which is absorbed by vegetation). It is an indication of vegetation density and possible changes in plant health.

## Slide 26: Yes, trees grow in SSA (data from LANDSAT)
https://www.globalforestwatch.org/map/country/MWI/

## Slide 27: Yes, trees grow in SSA (data from ALOS-PALSAR)
Carbon stock changes due to deforestation, degradation and (re)growth, with the values is the losses bar showing the percentage contribution of deforestation and degradation to the total carbon losses . Error bars show the 95% confidence intervals (CIs) and represent for the total error on each bar (from https://www.nature.com/articles/s41467-018-05386-z).
Notes: Radar imagery was obtained from the Phased Array L-Band Synthetic Aperture Radar sensor on-board JAXA’s Advanced Land Observation Satellite (ALOS-PALSAR). We use the 25 m horizontal-send vertical-receive (HV) polarisation mosaic product which provides annual maps of radar backscatter for 2007–201026 L-band HV backscatter is known to be sensitive to woody biomass density up to a saturation point of around 75 MgC ha−1 and has been shown to be able to detect deforestation, degradation, and regrowth in savanna woodlands.

## Slide 28: Yes, trees grow in SSA (data from MAXAR)
A 50-cm-scale image from 2002 (a) and a 50-cm-scale satellite image from 2021 (b) showing an agroforestry area at the same location. Tree cover has increased between 2002 and 2021 and the average carbon density of both areas was calculated and increased from 6 to 10 Mg ha−1. A large number of trees grow on farmlands, keeping the soils fertile and reducing the need for fallow periods. The greyscale of the background images indicates the carbon density per hectare, whereas the colour scale shows the carbon content of individual trees. This is a good example of the tree restoration monitoring potential in our study area (from https://www.nature.com/articles/s41586-022-05653-6).
Notes: 67% increase in woody biomass stocks
326,523 Maxar multispectral images from the QuickBird-2, GeoEye-1, WorldView-2 and WorldView-3 satellites collected from 2002 to 2020 from November to March from 9.5° N to 24° N latitude within Universal Transverse Mercator (UTM) zones 28–37 for Africa